## Slide 1: A Dipole with Grain Oriented Steel

## Slide 2: Problem Definition
Muon acceleration: use fast ramping dipoles + superconducting high field magnets
  Rep. rate: 1 kHz (+/-)
  B=-1.8 .. 1.8T
  Uses grain oriented steel
  D.Summers et al., arXiv:0707.0302

## Slide 3: Problem Definition
Prototype Dipole does not perform as expected
1.5T instead of 1.8T
Modelling correct?

## Slide 4: FEA Model
Opera 3D
  Magnetostatic simulation
  Explain drop in field
  (unsuitable for estimate on power loss)
Simulation based on modelling approach developed by VF
  Idea: break up internal iteration loop
  Linear elements, exploit symmetry
Included
  Anisotropic steel
  Packing factor 0.98

## Slide 5: VF Model
Grain orientation
300 mm
Gap: 1.5 mm
t = 50 mm

## Slide 6: Grain Oriented Steel
Data from AK Steel (TRAN-COR)
Factor 30+?

## Slide 7: BH Data
Data from: D. Summers. Fast Ramping 750 GeV Muon Synchrotron, Muon Acceleration Program (MAP). 27 Jun - 1 Jul 2011. Telluride, Colorado.

## Slide 8: μr: Polar Plot

## Slide 9: μr for various angles
μr
B (T)
Angle

## Slide 10: Simulation
BH data implemented in VF simulation
  For 0 and 90 degrees (insufficient data points for other angles)
  (functions based on tabular data with 2 or more variables possible)
Simulations: two sheets (+ boundary conditions)
  Magnet geometry as is
  Magnet geometry with ‘mitre’

## Slide 11: Magnetization and Vector Plot
H is low (mostly < 100 A/m) – mu_r =80..14000

## Slide 12: Field in Gap
1.483T
Relatively uniform

## Slide 13: Mitre Geometry
Same as before:
H is relatively low (<100 A/m)
Mu_r=80..14000

## Slide 14: Vector Plot

## Slide 15: Field in Gap

## Slide 16: Field in Gap (cont.)
B (T)
X (mm)
Mitre
Block

## Slide 17: Flux Jump Between Slabs
81 Wb (mitre: 76 Wb)

## Slide 18: Flux Between Slabs – Initial Geometry
37 Wb

## Slide 19: Flux Between Slabs – Mitre
24 Wb

## Slide 20: Future?
Estimate power loss
  Hysteresis loop necessary
  Can be implemented in Opera/ELEKTRA

## Slide 21: Summary
Previous assumptions too pessimistic – steel is not as anisotropic as feared initially
  Much better performance in general
Simulations can explain why new magnet design (mitre) performs as expected
  It does not explain why the old design did not work as expected…
Next steps?
  More data points on BH curve needed (at more angles)
  Power dissipation: Full magnetization / demagnetization curve required (at different fields)