## Slide 1: Report of High Pressurizing gaseous Hydrogen filled RF cavity experiment
K. Yonehara
on behalf of HPRF working group
APC, Fermilab
Muons, Inc.

## Slide 2: Goal of HPRF project
Demonstrate High Pressure RF cavity under high radiation condition
Study hydrogen plasma physics
Investigate RF breakdown from different aspect

## Slide 3: HPRF with beam
Find maximum acceptable beam intensity with pure GH2
  RF Q reduction
  Recovery time
Improve limitation of beam intensity
  Doping electro-negative gas
Optimize HPRF to apply various projects
  μ cooling channel for ν-Factory and μ-Collider
  μ acceleration at LBNL

## Slide 4: Design HPRF beamline
G-valve
Viewport of viewer
Viewer & storage
Beam pipe
400 MeV proton beam
from Linac
BPM
Two collimators
(solid: at operation mode
broken: pull collimator out to
change second collimator)
Beam absorber
5-T solenoid magnet
Collimator support rail
Faraday cup (?)
Waveguide
Coax cable
HP cavity
~ 1013 protons/RF pulse is generated in Linac
Change proton intensity by using various sizes of collimator and focusing magnet
Vacuum window

## Slide 5: Design collimator
A. Tollestrup
G4bl out:
Cavity plate and wall are invisible
Blue: collimator, beam absorber
Yellow hemisphere: Cu electrode
Light blue: Contour hole
White: Thread rod to hold electrode
Enlarged picture (yellow straight line: proton)
Upstream electrode is a hollow dome
Thickness of wall will be ~ 1mm

## Slide 6: Expected observation
Without SF6
With SF6
We assume Te = const. in this example.
However, Te = Te (Vc) in general.
Effects of recomb.
= saturation + linear recovery (>> RC)
Too much of SF6 (Z = 70, A = 146) will change electron dynamics.
e- + SF6  SF6-
e- + SF6  SF5- + F
Effects of
recomb.
M. Chung
p ~1000 psi
br ~ 10-8 cm3/s
32 mA H- ~ 2.5 x109 MIP

## Slide 7: Action item for first beam test
Radiation safety assessment
Design and make beam collimator and absorber
Modify RF cavity
Study modulation of RF wave
  Handle RF start timing to study recovery time of HPRF
Design and make beam position/current monitors
Re-configure RF waveguide
Install RF power circulator
Study flexibility of beam phase space

## Slide 8: Hydrogen plasma physics
Historic subject
But, it is still hot!
  Simplest system to test quantum mechanics, theory of many-body system, etc
  Nuclear fusion
  Astrophysics
Not many experiments and theories have been made in our HPRF condition
  Typically, they’ve investigated hydrogen plasma in DC, no B field, and
  relatively low gas density condition
  In our case, high RF E field, high B field, high gas density, low temperature,
and high radiation in near future
Our interest is recombination process

## Slide 9: Polyatomic hydrogen
e- + H2+ → 2H < 70 ns
(T. Oka suggested)
H3+ + H2+ H2 → H5+ + H2 3 × 10-15 s (T. Oka suggested)
H3+, H5+, H7+,… can be formed in very short
time (10-15 s) via three body interaction
Unfortunately, no de-excitation light in
electron recombination process
A. Tollestrup
Updated by KY

## Slide 10: Recombination process
Z. Insepov
H2+ + e- → 2H (+ hν)
σmax ~10-14 cm2
(α > 10-8 cm3/s, ne ~ 1014 electrons/cm3)
H2+ + e- → H+ + H-
σ = 3 × 10-18 cm2 @ Ke = 1 eV
H2+ + e- → H2 + hν
β ~ 10-15 cm3/s @ Te = 10000 K
Primary channel:
Polyatomic state:
Challenge in simulation:
Above values are obtained from dilute condition
Density effect will be dominant in the HPRF condition
Reaction kinetics in a dense gas is diffusion-limited
Polyatomic hydrogen seems to be coherent state
It may requires many-body quantum mechanics

## Slide 11: New approach: Optical measurement
Gap = 3 cm

## Slide 12: Observed optical signal
656 nm
500 nm
Two spectroscopic measurements have made at GH2 pressure 620 and 810 psi
Applied electric fields were ~42 MV/m at 620 psi and ~47 MV/m at 810 psi, respectively
Applied RF pulse length was 20 μs
Above spectrum were taken in spectrometer as monochromatic mode and averaged over
50 breakdown lights at GH2 pressure 620 psi
Resolution of spectrometer is 2 nm
656 nm is on H-alpha line
Cu lines are spread in VIS region, i.e. it covers around 500 nm but atomic H does not have
any lines around it (ref. NIST)

## Slide 13: Spectroscopy in HPRF
620 psi
810 psi
H-alpha line (656 nm)
H-beta line (480 nm)
A point is the integrated PMT signal that is shown in previous slide
Data are calibrated with wavelength dependence on PMT

## Slide 14: Decay time
620 psi
810 psi
Decay time seems to be more sensitive on the resonance line
With and size of τ-1 are changed by GH2 pressure

## Slide 15: Observations in optical measurement
We confirmed that a light was produced in the HPRF cavity only when a breakdown happened, where the breakdown is that the RF cavity releases significant amount of RF power in a very short time
We observed one large peak around 656 nm and one small peak around 480 nm in breakdown spectra
The width of each peak is (unexpectedly) broadened
We observed a high intensity continuum spectrum
We observed strong correlation between PMT decay time and wavelength
The observed rise time of PMT signal is 5 ~ 10 ns, this time scale is reasonably matched to the observed decay time of electric and magnetic probes (10 ~ 15 ns)
However, there is a dependence on wavelength and PMT rise time, e.g. τ ≈ 10 ns at λ = 656 nm, τ ≈ 5 ns at λ = 400 nm
Decay time at λ = 656 nm is 500 ns which is well matched with Einstein coefficient
Decay time at λ = 400 nm is 60 ns

## Slide 16: RF breakdown in dense GH2
Experimental facts:
  Cavity is insensitive to B field by filling dense GH2
  Maximum E field is determined by gas density at gas breakdown region
  Maximum E field seems to saturate at metallic breakdown region

## Slide 17: Maximum E vs GH2 pressure
1.0
0.1
0.01
0.002
0.005
0.001
0.0005
0.0001
0
Probability
Nov, 2009 run

## Slide 18: Maximum E vs GH2 pressure
1.0
0.1
0.01
0.002
0.005
0.001
0.0005
0.0001
0
Probability
Sep., 2008 run
Nov, 2009 run
Compare with previous result

## Slide 19: Probability of breakdown
Long run (10~20k RF pulses)
620 psi
1150 psi
: # of breakdowns
: # of RF pulses
BD probability curve is very clear shape at low pressure region
Boundary becomes fuzzy at high pressure region (> ~1000 psi)
Normal run (1k RF pulses)

## Slide 20: Questions
RF power decays in 10 ~ 20 ns at breakdown event while propagation of plasma only makes a few mm in this time scale. How does electronic breakdown happens?
PMT signal seems to be observed only when breakdown takes place. If some amount of field emission electrons exist in the HPRF why they do not induce de-excitation light? Poor light sensitivity or no high energy electron?
RF pickup probe
RF reflection pwr
RF forward pwr
PMT signal
Have we ever seen any evidence of electron accumulation process even there must be a lot of field emission electrons?
Electron energy distribution
(Red: E/P < 14 V/cm/mmHg
Blue: E/p > 14 V/cm/mmHg)
A. Tollestrup
A. Tollestrup

## Slide 21: Timetable for HPRF project
Jan., 2010 HPRF with no beam test
Spring 2010 First beam test
Summer 2010 Second beam test, test proto-type HPRF
Winter 2010 Third beam test, test dielectric loaded RF
2011~ 6D cooling demo experiment

## Slide 22: Conclusions
Start preparing first beam test
  Design collimator to vary beam intensity
Non-beam test analysis has been made from two successful runs (Sep. ’08 and Nov. ’09)
  Always observed a big spark light at breakdown
  But, no de-excitation light without breakdown is observed
  Need to find out why we do not see it