Report of Project Manager

Michael S. Zisman

Center for Beam Physics

Muon Collaboration Project Manager

MUTAC Review–BNL

April 28–29, 2004

•	Introduction

•	FY03 accounting

•	FY03 R&D accomplishments

•	FY04 budget

•	FY04 plans

•	Summary and outlook

•	In FY03, the MC budget was halved

—	$2.809M($1.429M

| Year | DOE-base ($M) | DOE-MC ($M) | TOTAL ($M) |
| --- | --- | --- | --- |
| FY00 | 3.3 | 4.7 | 8.0 |
| FY01 | 3.0 | 3.2 | 6.2 |
| FY02 | 3.0 | 2.8 | 5.8 |
| FY03 | 2.2 | 1.4 | 3.6 |
| FY04 | 2.2 | 1.4 | 3.6 |
| FY05a) | 2.2 | 1.4 | 3.6 |

a)Present DOE guidance.

•	We had anticipated restoration to FY02 level in FY04

—	no such luck!

•	By juggling projects across fiscal year boundaries and careful prioritization, we have continued to make progress

—	this was recognized by MUTAC and MCOG last year

•	Hardware development continues as major focus of FY04 activity

•	Simulation effort aimed at ring coolers made good progress last year

—	appears more relevant for Muon Collider than Neutrino Factory

—	FFAG work also making good progress

•	Effort toward MICE proposal is coming to fruition

—	now have scientific approval from RAL

o	but still no real funding

•	Here I will cover:

—	FY03 accounting and R&D accomplishments

—	FY04 budget and plans

•	FY03 budget finalized by Spokespersons and PM in November

•	FY03 budget was tight ($1.429M ( $1.403M)

•	Supplemental funding request submitted in May, 2002

—	and subsequently ignored

•	Simulations and Theory group reconstituted by Spokespersons in FY03

—	led by R. Raja, with lieutenants for various subgroups

—	now led by R. Fernow

•	Another “initiative” requiring resources: International Muon Ionization Cooling Experiment

—	investment in our future, but non-trivial to accommodate

—	presently requires mostly “effort” (base program funds)

o	this is changing as engineering is becoming necessary

•	FY03 MC budget (approved by MCOG):

| Institution | COOLING | TARGETRY | COLLIDER | EFFORTa | RESERVEb | TOTAL ($K) |
| --- | --- | --- | --- | --- | --- | --- |
| BNL |  | 300 |  |  |  | 300 |
| FNAL | 400 |  |  |  |  | 400 |
| LBNL | 204 |  |  |  | 26c | 320 |
| ANL |  |  |  | 144 |  | 144 |
| IIT |  |  |  | 75 |  | 75 |
| Mississippi |  |  |  | 50 |  | 50 |
| Princeton |  | 50 |  |  |  | 50 |
| UCB |  |  | 5 |  |  | 5 |
| UCLA | 25 |  | 50 |  |  | 75 |
| UCR |  |  | 90 |  |  |  |
| ORNL |  |  |  |  |  | 0 |
| JLab |  |  |  | 10 |  | 10 |
| TOTAL ($K) | 629 | 350 | 145 | 279 | 26 | 1429 |

aIncludes beam simulation and diagnostics effort.

bModest project reserve used to account for uncertainties in R&D activity costs.

cEventually lost due to “recision” by DOE late in the year.

•	Also: salary support from BNL, FNAL, LBNL; support from NSF (mainly Cornell) of ($1M; and support from ICAR ((12 FTE)

•	Supplemental request submitted to DOE in May, 2002 (priority order)

—	priorities decided in discussions at Shelter Island

o	no response from DOE

| Item | Request ($K) |
| --- | --- |
| 0) AGS operation | 50 |
| 1) 201 MHz RF cavity fabrication | 350 |
| 2) Targetry magnet fabrication | 400 |
| 3) Cooling simulation effort | 200 |
| 4) 805 MHz RF cavity R&D | 100 |
| 5) LH2 absorber fabrication | 100 |
| 6) Target studies | 50 |
| 7) Solenoid coil design | 150 |
| 8) Target simulations | 50 |
| TOTAL | 1450 |

•	Main goals for FY03

—	engineer target test magnet

—	continue development of MUCOOL Test Area (MTA) at FNAL

—	continue high-power tests of 805 MHz cavity

—	continue 201-MHz SCRF development (NSF supported)

—	continue with LH2 absorber development (includes ICAR support)

—	begin fabrication of 201-MHz NCRF cavity

—	submit technical proposal for MICE

—	continue exploring and optimizing cooling ring and FFAG performance

•	Aspirations modest this year due to severe budget shortfall

•	Before funds were distributed, each institution provided milestones agreed upon by PM

—	milestones (example below) reflect budget allocations for each institution, including base program funds

•	Summary of FY03 spending is shown below

•	Accounting summary made for each institution

•	Along with list of accomplishments

•	Developed engineering design and cost estimate for 15-T targetry test solenoid

•	Developed continuous-flow Hg jet at 2 m/s

•	Measured properties of Super-Invar and inconel samples after irradiation

•	Continued design and simulation studies of conventional-magnet (dipole, quadrupole) cooling rings

•	Carried out simulation studies for solenoid-based ring cooler

•	Continued evaluation of alternative FFAG accelerators

•	Added time-of-flight capability into G4MICE package

•	Simulated baseline and alternative configurations for MICE

•	Scorecard of milestones also prepared at the end of the year

•	Complete summary report given to MCOG and DOE each year

—	available in your handout

•	R&D progress being made on all fronts:

—	Targetry (McDonald, Samulyak, Kirk)

—	Cooling (Bross, Li, Torun, Errede, Cummings, Ishimoto, Johnson)

—	Acceleration (Berg)

—	Simulations (Fernow, Palmer)

•	Overview presented here; details to follow

•	Radiation testing of candidate solid-target materials (Super-Invar and Inconel) carried out at BNL with 200 MeV p beam

—	looked at both CTE and tensile strength changes

o	big changes in Super-Invar CTE with dose, less with Inconel

o	yield strength increases but material gets more brittle

•	Contract awarded for 5–15 T magnet fabrication (for E951 at BNL?)

| Stage | Field (T) | Power (MW) | Coolant | Temperature (K) |
| --- | --- | --- | --- | --- |
| 1 | 5 | 0.6 | N2 | 84 |
| 2 | 10 | 2.2 | N2 | 74 |
| 3 | 15 | 2.2 | H2 | 30 |
| 3a | 15 | 4.5 | N2 | 70 |

—	looking seriously into using battery power (suggested originally by Summers)

Battery and charger (12 V, 1400 A)		Mechanical switch for 4.4 MW

—	if power supply fails, we call AAA!

•	Developed a 2.5 m/s continuous Hg jet system for E951 at Princeton

—	never used with beam due to elimination of AGS HEP running

—	Wood’s metal (heated) version was started but put on hold for now

Test apparatus					Mercury jet…on a good day

•	Present tests use pillbox cavity with replaceable windows (or grids) (Li)

—	cavity fits in bore of Lab G solenoid

•	Pillbox cavity reached 40 MV/m in Lab G with no solenoid field

—	with solenoid performance worse (18 MV/m), radiation levels higher

•	With TiN-coated Be windows no conditioning problems seen without magnetic field

(	parallel plate geometry does not cause big problems

•	Found no damage to Be surface, but sputtered Cu is present

—	suggests need to focus more on copper body than on windows

•	Backgrounds lower with Be than Cu

Be windows with sputtered copper

•	Workshop on high-gradient rf limitations was held at ANL, October 7–9, 2003

—	URL: http://www.mice.iit.edu/rfworkshop/

•	201 MHz rf cavity under construction (Li, Virostek, Rimmer)

—	completion in about 1 year

o	Jlab and U-Miss collaborating on cavity fabrication

Setup for welding stiffener ring			 After e-beam weld to half-shell

•	Ideal cavity termination would be perfectly conducting and transparent to muon beam, and would not affect cavity frequency

—	we now propose pre-curved windows that bow predictably

o	with proper design, stresses remain quite low as the foil heats

•	Ordered shaped Be foils from Brush-Wellman to test at 805 MHz

•	Absorber group has developed strong, thin windows (Cummings, Kaplan)

—	windows as thin as 125 (m machined from solid Al (Summers)

—	new stronger ((thinner) design (Lau) to be built and tested next

—	none built last year, but fabrication of first window done now

o	will destruction-test a series of windows to certify design

•	To test hardware, built MUCOOL Test Area at Fermilab (Popovic)

—	absorber, solenoid, and 201 MHz rf cavity will be integrated here

Completed MTA (as seen by Project Manager)

Completed MTA (as seen by Lab Director)

•	Work on 201 MHz scrf cavity for the acceleration system made good progress (Hartill, Padamsee; NSF)

—	reached 11 MV/m after re-cleaning cavity

o	low-power Q0 = 2 x 1010 (at 2.5 K)

—	now trying to understand Q slope in terms of impurities and Nb coating properties

o	cavity being recoated at CERN

•	Simulations

—	significant effort on emittance exchange

—	ring coolers (Balbekov, Palmer) important due to potentially significant cost reduction (for Muon Collider)

o	6D cooling looks promising; injection is an issue

—	dipole rings also being explored; some configurations look promising

•	Looking at alternative acceleration schemes

—	RLA with FFAG arcs (Berg, Johnstone, Keil, Sessler, Trbojevic)

—	very rapid cycling booster (Summers)

—	discussion of building an electron model of FFAG has started

o	would need to identify funding and host institution

–	proposed for U.S.-Japan funds; TRIUMF as host?

o	hard to see how to pry this out of existing budgets

•	Prepared initial budget for FY04 based on present budget guidance

—	Tech Board met three times to discuss it

—	original guidance was (sadly) accurate

•	Given so many uncertainties, we have chosen to maintain a reasonable reserve despite the low funding

—	money for this was available due to the failure to hire a simulations post-doc last year

•	A small amount of funding will be transferred to BNL for offsetting travel expenses of consultants

—	this allows me to off-load some of the administrative work to Kathy Tuohy

•	MCOG approved budget in February

•	Budgetary goal is to maintain university programs while making some progress on key fabrication activities

•	FY04 MC budget (only DOE-MC funds)t

| Institution | COOLING | TARGETRY | ACCEL./ COLLIDER | EFFORTa | RESERVE | TOTAL ($K) |
| --- | --- | --- | --- | --- | --- | --- |
| BNL |  | 275 | 10 |  |  | 285 |
| FNAL | 400 |  |  |  |  | 400 |
| LBNL | 100 |  |  |  | 104 | 204 |
| ANL |  |  |  | 144 |  | 144 |
| IIT |  |  |  | 77 |  | 77 |
| Mississippi | 50 |  |  |  |  | 50 |
| Princeton |  | 50 |  |  |  | 50 |
| UCB | 5 |  |  |  |  | 5 |
| UCLA | 25 |  | 50 |  |  | 75 |
| UC-Riverside |  |  |  |  |  | 0 |
| ORNL |  |  |  |  |  | 0 |
| Jlab | 110 |  |  |  |  | 110 |
| TOTAL ($K) | 690 | 325 | 60 | 221 | 104 | 1400 |

aIncludes beam simulation and diagnostics effort.

tAlso: salary support from BNL, FNAL, LBNL; support from NSF (mainly Cornell) of $1M; and support from ICAR ((12 FTE)

•	Supplemental request submitted to DOE in September, 2003 (priority order)

—	priorities decided in discussions between Spokespersons and PM

o	no response from DOE…again!

| Item | Request ($K) |
| --- | --- |
| 1) 201 MHz RF testing | 400 |
| 2) LH2 absorber test capability | 460 |
| 3) Targetry magnet fabrication | 400 |
| 4) Coupling coil design and construction | 300 |
| TOTAL | 1560 |

•	Targetry

—	complete fabrication of 15 T magnet and begin power supply

•	Cooling

—	complete fabrication of 201 MHz high-gradient cavity (17 MV/m)

—	test convection-cooled LH2 absorber with all safety aspects

•	Acceleration

—	continue effort to increase 201 MHz SCRF cavity gradient

•	Simulations

—	develop cost-optimized front-end for APS Study

—	continue design work on FFAG-based systems

•	MICE

—	continue to seek funding

•	Equatorial weld completed

—	a “cavity” at last!

•	The past year was productive for the MC

—	fabrication of Targetry test magnet started

—	NCRF cavity tests made progress (at 805 MHz)

—	201 MHz NCRF cavity fabrication launched

—	approaches to study cooling rings and FFAG rings developed

—	improved absorber window design developed

—	SCRF cavity testing reached 11 MV/m

•	MICE gaining momentum

—	scientific approval from RAL; U.S. funding proposal under review

•	Strong MUTAC and MCOG endorsements of R&D accomplishments and plans will hopefully help our budget eventually

—	the MC is certainly continuing to hold up its end of the bargain!

# Text boxes

Yield (MPa)

dpa

Cu windows

Be windows

Grain-oriented Si steel